## Slide 1: The AUTOPIA Driver
Enrique Onieva Caracuel
Industrial Computer Science Department.
Centro de Automática y Robótica – Consejo Superior de Investigaciones Científicas
enrique.onieva@car.upm-csic.es
IEEE-CIG 2010 Simulated Car Racing Competition
Genetic Algorithms and Driving Heuristics in Car Racing

## Slide 2: Architecture Schema
Three basic modules:
  Gear control:
    Basic gear control based on rpm
    Simple stuck detection and management
  Steering control
  Speed control
Opponents Module:
  Acts on steering and brake signal to overtake opponents and avoid collisions.
Learning Module in Warm-up Stage
  Factor over the target speed in certain track segments

## Slide 3: Speed Module
TargetSpeed = TS1·T(0)
      + TS2*max(T(5),T(-5)) + TS3*min(T(5),T(-5))
      + TS4*max(T(10),T(-10)) + TS5*min(T(10),T(-10))
    T(X)  Track Measure of Sensor Oriented at X degress
    [TS1,TS2,TS3,TS4,TS5]: values optimized by Genetic Algorithm
  Diff = Speed – TargetSpeed
  Accel & Brake:
Outside of the Track Axis:
  Brake = 0
  Throttle = 0.3 if speed < 75
  Throttle = 0.6 otherwise
ABS Filter when braking.

## Slide 4: Steering Control
Steering= ST1*a
  + ST2*(((ar1*tr1)+(al1*tl1))/(tl1+tr1))
  + ST3*(((ar2*tr2)+(al2*tl2))/(tl2+tr2))
  + ST4*(((ar3*tr3)+(al3*tl3))/(tl3+tr3))
  a: angle of the maximum track reading
  ar1, al1, tr1, tl1: angle and track measure of right and left first neighbors to ‘a’
  ar2, al2, tr2, tl2: angle and track measure of right and left second neighbors to ‘a’
  ar3, al3, tr3, tl3: angle and track measure of right and left thid neighbors to ‘a’
  [ST1,ST2,ST3,ST4,ST5]: values optimized by Genetic Algorithm
  Additionally: Use only the angle when much free distance
    if (|position|<0.75 AND (a=0 || T(9)>ST5*speed/3.6)
    Steering= 0.5*Angle;

## Slide 5: Basic Modules Optimization
Steady State Genetic Algorithm.
  Double vector representation
    {TS1,TS2,TS3,TS4,TS5,ST1,ST2,ST3,ST4,ST5}
  Binary Tournament Selection
  BLX-ALPHA crossover
  Uniform Mutation
  Initial population of 50 individuals

## Slide 6: Basic Modules Optimization
  Fitness function:
    Sum of distances traveled after running 60 seconds alone along 4 different tracks.
    Distance = 0 if the vehicle goes out of the track or suffers damage.
  Result After 100 Generations:
    {ST1,ST2,ST3,ST4,ST5,TS1,TS2,TS3,TS4,TS5}
    {0.21,1.56,0.68,0.53,1.25, 1.08,1.79,0.02,0.75,0.13}

## Slide 7: Opponents Management (Steering)
Heuristic Rule System:
  If O(-20,-10,10,20) detects an opponent with lateral displacement less than 20 meters, move the steering trackwidth/100 through the direction with more free distance.
  If O(-40,-30,-20,-10) detects an opponent with lateral displacement less than 20 meters, move the steering trackwidth/50 through the right.
  If O(-70,-60,-50)<15 meters, move the steering trackwidth/50 through the right.
  If O(-140,-130,-120,-110,-100,-90,-80)<15meters , move the steering trackwidth/50 through the right.
  Mirroring actions for positive sensors
  O(X)  Opponent Measure of Sensor Oriented at X
Steering Modification limited to 0.35

## Slide 8: Opponents Management (Brake)
Brake = 10% if:
  Speed>100 AND O(-20,-10,10,20) detects an opponent with lateral displacement less than 4 meters and O(-20,-10,10,20) is decreasing more than 15m/s.
  Speed>50 AND O(-20,-10,10,20) detects an opponent with lateral displacement less than 2 meters.
Brake is maintained during D steps to make the driver more cautious in function of the damage:
  D=2+3*round(damage/1000)

## Slide 9: Learning Module (Warm-Up)
Running normally in warm-up stage.
  Maintain a vector with as many real values as tracklength in meters.
  Vector initialized to 1.0
  If the vehicle goes out of the track or suffers damage then multiply vector positions from 250 meters before the current position by 0.9.
  If the vehicle JUMPS then multiply vector positions from 15 meters before the current position by 0.5.
Vector is multiplied by F to make the driver more cautious in function of the damage:
  F=1-0.02*round(damage/1000)